## Slide 1: Mobile Communications Chapter 5: Wireless LANs
Characteristics
IEEE 802.11 (PHY, MAC, Roaming, .11a, b, g, h, i, n … z, ac, ad, …, ax, ay, az, ba, bb, …)
Bluetooth / BLE / IEEE 802.15.x / ZigBee
IEEE 802.16/.19/.20/.21/.22
Comparison

## Slide 2: Mobile Communication Technology according to IEEE (examples)
Local wireless networks
WLAN 802.11
802.11a
802.11b
802.11i/e/…/n/…/z/az/ba/bb…
802.11g
WiFi
802.11h
Personal wireless nw
WPAN 802.15
802.15.4
802.15.1
802.15.2
Bluetooth
802.15.4a/b/c/d/e/f/g…y/z
ZigBee
802.15.3
Wireless distribution networks
WMAN 802.16 (Broadband Wireless Access)
[hist.: 802.20 (Mobile Broadband Wireless Access)]
802.16e (addition to .16 for mobile devices)
+ Mobility
WiMAX
802.15.3b/c/d/e/f
802.15.5, .6 (WBAN), .7, .8, .10… .15
(see: http://www.ieee802.org/11/QuickGuide_IEEE_802_WG_and_Activities.htm)
(see: http://www.ieee802.org/15/)

## Slide 3: Characteristics of wireless LANs
Advantages
  very flexible within the transmission area
  ad-hoc networks without previous planning possible
  (almost) no wiring difficulties (e.g. historic buildings, firewalls)
  more robust against disasters like, e.g., earthquakes, fires - or users pulling a plug...
Disadvantages
  typically lower user data rates/higher delays and delay jitter compared to wired networks due to shared medium, lots of interference (it depends on your neighbors!)
  different/proprietary solutions, especially for higher bit-rates or low-power, standards take their time, devices have to fall back to older/standard solutions
  products have to follow many national restrictions if working wireless, it takes longer time to establish global solutions

## Slide 4: Design goals for wireless LANs
global, seamless operation
low power for battery use
no special permissions or licenses needed to use the LAN
robust transmission technology
simplified spontaneous cooperation at meetings
easy to use for everyone, simple management
protection of investment in wired networks
security (no one should be able to read my data), privacy (no one should be able to collect user profiles), safety (low radiation)
transparency concerning applications and higher layer protocols, but also location awareness if necessary
…

## Slide 5: Comparison: infrastructure vs. ad-hoc vs. mesh networks
infrastructure network
ad-hoc network
AP
AP
AP
wired network
AP: Access Point
mesh network

## Slide 6: 802.11 – Classical architecture of an infrastructure network
Station (STA)
  terminal with access mechanisms to the wireless medium and radio contact to the access point
Basic Service Set (BSS)
  group of stations using the same radio frequency
Access Point
  station integrated into the wireless LAN and the distribution system
Portal
  bridge to other (wired) networks
Distribution System
  interconnection network to form one logical network (EES: Extended Service Set) based on several BSS
Distribution System
Portal
802.x LAN
Access
Point
802.11 LAN
BSS2
802.11 LAN
BSS1
Access
Point
STA1
STA2
STA3
ESS
Notes: 9

## Slide 7: 802.11 - Architecture of an ad-hoc network
Direct communication within a limited range
  Station (STA): terminal with access mechanisms to the wireless medium
  Independent Basic Service Set (IBSS): group of stations using the same radio frequency
802.11 LAN
IBSS2
802.11 LAN
IBSS1
STA1
STA4
STA5
STA2
STA3

## Slide 8: 802.11 - Architecture of a mesh network
Distribution
System
Mesh BSS forming a meshed network with possibly redundant paths using the Hybrid Wireless Mesh Protocol (HWMP)
Mesh Gate, AP and DS can be co-located in one device
Distribution
System
Portal
802.x LAN
Mesh
Gate
Mesh BSS
802.11 LAN
BSS
Access
Point
STA1
Mesh STA1
Mesh STA2
Mesh
Gate
Mesh STA3
Mesh STA4
Mesh STA5
802.11 LAN
BSS
Access
Point
STA2

## Slide 9: IEEE standard 802.11
mobile terminal
access point
fixed
terminal
application
TCP
802.11 PHY
802.11 MAC
IP
802.3 MAC
802.3 PHY
application
TCP
802.3 PHY
802.3 MAC
IP
802.11 MAC
802.11 PHY
LLC
infrastructure
network
LLC
LLC

## Slide 10: 802.11 - Layers and functions
MAC
  access mechanisms, fragmentation, encryption
MAC Management
  synchronization, roaming, MIB, power management
PHY
  clear channel assessment (carrier sense)
  modulation, coding
PHY Management
  channel selection, MIB
Station Management
  coordination of all management functions
PHY
MAC
LLC
MAC Management
PHY Management
PHY
DLC
Station Management

## Slide 11: Questions & Tasks
  Check the relevant web pages – it is a very dynamic field!
  How is mobility restricted using WLANs? What additional elements are needed for roaming between networks, how and where can WLANs support roaming? In your answer, think of the capabilities of layer 2 where WLANs reside.
  What are the basic differences between wireless WANs and WLANs, and what are the common features? Consider mode of operation, administration, frequencies, capabilities of nodes, services, national/international regulations.

## Slide 12: 802.11 - Physical layer (historical – not in standard any longer)
3 versions: 2 radio (typ. 2.4 GHz), 1 IR
  data rates 1 or 2 Mbit/s
FHSS (Frequency Hopping Spread Spectrum) - obsolete
  spreading, despreading, signal strength, typ. 1 Mbit/s
  min. 2.5 frequency hops/s (USA), two-level GFSK modulation
DSSS (Direct Sequence Spread Spectrum) – many products
  DBPSK modulation for 1 Mbit/s (Differential Binary Phase Shift Keying), DQPSK for 2 Mbit/s (Differential Quadrature PSK)
  preamble and header of a frame is always transmitted with 1 Mbit/s, rest of transmission 1 or 2 Mbit/s
  chipping sequence: +1, -1, +1, +1, -1, +1, +1, +1, -1, -1, -1 (Barker code)
  max. radiated power 1 W (USA), 100 mW (EU), min. 1mW
Infrared - obsolete
  850-950 nm, diffuse light, typ. 10 m range
  carrier detection, energy detection, synchronization

## Slide 13: DSSS PHY packet format (legacy)
Synchronization
  synch., gain setting, energy detection, frequency offset compensation
SFD (Start Frame Delimiter)
  1111001110100000
Signal
  data rate of the payload (0A: 1 Mbit/s DBPSK; 14: 2 Mbit/s DQPSK)
Service
  future use, 00: 802.11 compliant
Length
  length of the payload
HEC (Header Error Check)
  protection of signal, service and length, x16+x12+x5+1
synchronization
SFD
signal
service
HEC
payload
PLCP preamble
PLCP header
128
16
8
8
16
variable
bits
length
16

## Slide 14: IEEE 802.11 HR/DSSS – PHY frame formats (was 802.11b)
High Rate Direct Sequence Spread Spectrum @ 2.4GHz
Data rate
  1, 2, 5.5, 11 Mbit/s, depending on SNR
  User data rate max. approx. 6 Mbit/s
synchronization
SFD
signal
service
HEC
payload
PLCP preamble
PLCP header
128
16
8
8
16
variable
bits
length
16
192 µs at 1 Mbit/s DBPSK
1, 2, 5.5 or 11 Mbit/s
short synch.
SFD
signal
service
HEC
payload
PLCP preamble
(1 Mbit/s, DBPSK)
PLCP header
(2 Mbit/s, DQPSK)
56
16
8
8
16
variable
bits
length
16
96 µs
2, 5.5 or 11 Mbit/s
Long PLCP PPDU format
Short PLCP PPDU format (optional)

## Slide 15: Channel selection (non-overlapping)
2400
[MHz]
2412
2483.5
2442
2472
channel 1
channel 7
channel 13
Europe (ETSI)
US (FCC)/Canada (IC)
2400
[MHz]
2412
2483.5
2437
2462
channel 1
channel 6
channel 11
22 MHz
22 MHz

## Slide 16: IEEE 802.11 OFDM – PHY frame format (was 802.11a)
Orthogonal Frequency Division Multiplexing @ 5GHz
Data rates
  E.g. 6, 9, 12, 18, 24, 36, 48, 54 Mbit/s, depending on SNR and channel width
  User throughput (1500 byte packets): 5.3 (6), 18 (24), 24 (36), 32 (54)
  6, 12, 24 Mbit/s mandatory
Transmission range
  100m outdoor, 10m indoor
    E.g., 54 Mbit/s up to 5 m, 48 up to 12 m, 36 up to 25 m, 24 up to 30m, 18 up to 40 m, 12 up to 60 m
Frequency
  Free 5.15-5.25, 5.25-5.35, 5.725-5.825 GHz ISM-band
rate
service
payload
variable
bits
6 Mbit/s
PLCP preamble
signal
data
symbols
12
1
variable
reserved
length
tail
parity
tail
pad
6
16
6
1
12
1
4
variable
6, 9, 12, 18, 24, 36, 48, 54 Mbit/s
PLCP header

## Slide 17: Operating channels of 802.11a in Europe (examples)
5150
[MHz]
5180
5350
5200
36
44
16.6 MHz
center frequency =
5000 + 5*channel number [MHz]
channel
40
48
52
56
60
64
5220
5240
5260
5280
5300
5320
5470
[MHz]
5500
5725
5520
100
108
16.6 MHz
channel
104
112
116
120
124
128
5540
5560
5580
5600
5620
5640
132
136
140
5660
5680
5700

## Slide 18: Operating channels for 802.11a / US U-NII (examples)
5150
[MHz]
5180
5350
5200
36
44
16.6 MHz
center frequency =
5000 + 5*channel number [MHz]
channel
40
48
52
56
60
64
149
153
157
161
5220
5240
5260
5280
5300
5320
5725
[MHz]
5745
5825
5765
16.6 MHz
channel
5785
5805

## Slide 19: OFDM in IEEE 802.11
OFDM with 52 used subcarriers (64 in total)
  48 data + 4 pilot
    (plus 12 virtual subcarriers)
  312.5 kHz spacing
subcarrier
number
1
7
21
26
-26
-21
-7
-1
channel center frequency
312.5 kHz
pilot

## Slide 20: IEEE 802.11 ERP – PHY frame formats (was 802.11g)
Extended Rate PHY @ 2.4GHz
Data rates
  Builds on classical 1, 2 Mbit/s (DSSS) and 1, 2, 5.5, 11 Mbit/s (HR DSSS)
  Uses additionally OFDM for 6, 9, 12, 18, 24, 36, 48, and 54 Mbit/s (thus check 802.11 OFDM for frame formats)
Many more options and modulation modes standardized but obsolete or deprecated.
Basically, it applies the old 802.11a @ 2.4 GHz.

## Slide 21: IEEE 802.11 HT – PHY frame formats (was 802.11n) – marketed as WiFi 4
High Throughput (HT) Orthogonal Frequency Division Multiplexing (OFDM) system @ 2.4 and 5 GHz
Based on the OFDM system, but now using up to 4 spatial stream operating in 20 MHz bandwidth (additionally, 40 MHz bandwidth specified offering up to 600 Mbit/s)

## Slide 22: IEEE 802.11 HT – PHY frame formats (was 802.11n)

## Slide 23: Very High Throughput (VHT) PHY – uses OFDM (was 802.11ac)
Source: IEEE Std 802.11-2016

## Slide 24: IEEE 802.11 VHT – High-speed for WLANs at 5 GHz – marketed as WiFi 5
Single link throughput > 500Mbit/s, multi-station > 1 Gbit/s
Bandwidth up to 160 MHz (80 MHz mandatory), up to 8x MIMO, up to 256 QAM, beamforming, SDMA via MIMO
Example home configuration:
  8-antenna access point, 160 MHz bandwidth, 6.77 Gbit/s
  4-antenna digital TV, 3.39 Gbit/s
  2-antenna tablet, 1.69 Gbit/s
  Two 1-antenna smartphones, 867 Mbit/s each
Redefinition of many protocol fields and procedures!

## Slide 25: Questions & Tasks
  Why is the number of non-overlapping channels important?
  Why is the user throughput much lower than the max. available data rate at PHY?
  What are advantages of higher frequency bands? Disadvantages?
  How are higher data rates achieved?

## Slide 26: 802.11 - MAC layer architecture
Source: IEEE Std 802.11-2016

## Slide 27: How to access the medium in 802.11
Distributed Coordination Function (DCF)
Fundamental access method in 802.11, mandatory
Also known as CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance)
Random backoff, certain fairness, refinement with RTS/CTS possible
Point Coordination Function (not really used, will be kicked out of the standard in the future)
Contention free access, reservation of the medium
Hybrid Coordination Function (HCF)
QoS support by combining DCF and PCF
Contention-based channel access (Enhanced Distributed Channel Access, EDCA) and controlled channel access (HCF Controlled Channel Access, HCCA)
Support of different priorities for, e.g., background, best effort, video, voice traffic (WiFi WMM Designations)
Mesh Coordination Function (MCF)
Only in a MBSS, EDCA for contention-based access, MCCA (MCS Controlled Channel Access) for contention-free access

## Slide 28: 802.11 - MAC Inter Frame Space
Priorities of packets defined through different inter frame spaces (not always guaranteed)
  RIFS (Reduced IFS)
    shortest IFS, reduced overhead, only if no SIFS expected, for higher throughput
  SIFS (Short IFS)
    for ACK, CTS, polling response
  PIFS (PCF IFS)
    used to gain priority access (PCF, TIM, …)
  DIFS (DCF IFS)
    for “normal” asynchronous data service
  AIFS (Arbitration IFS)
    variable depending on QoS
  EIFS (Extended IFS)
    IFS e.g. after an incorrect FCS
  Additional “beamforming” IFSs
t
medium busy
SIFS
PIFS
DIFS
DIFS
next frame
contention
direct access if medium is free  DIFS
RIFS
AIFSi
AIFSi
EIFS
…

## Slide 29: 802.11 - CSMA/CA access method I
station ready to send starts sensing the medium (Carrier Sense based on CCA, Clear Channel Assessment)
if the medium is free for the duration of an Inter-Frame Space (IFS), the station can start sending (IFS depends on service type)
if the medium is busy, the station has to wait for a free IFS, then the station must additionally wait a random back-off time (collision avoidance, multiple of slot-time)
if another station occupies the medium during the back-off time of the station, the back-off timer stops (fairness)
t
medium busy
DIFS
DIFS
next frame
contention window
(randomized back-off mechanism)
slot time (20µs)
direct access if medium is free  DIFS
Notes: 12

## Slide 30: 802.11 - Competing stations - simple version
t
busy
boe
station1
station2
station3
station4
station5
packet arrival at MAC
DIFS
boe
boe
boe
busy
elapsed backoff time
bor
residual backoff time
busy
medium not idle (frame, ack etc.)
bor
bor
DIFS
boe
boe
boe
bor
DIFS
busy
busy
DIFS
boe
busy
boe
boe
bor
bor

## Slide 31: 802.11 - CSMA/CA access method II
Sending unicast packets
  station has to wait for DIFS before sending data
  receivers acknowledge at once (after waiting for SIFS) if the packet was received correctly (FCS)
  automatic retransmission of data packets in case of transmission errors, but exponential increase of contention window
t
SIFS
DIFS
data
ACK
waiting time
other
stations
receiver
sender
data
DIFS
contention

## Slide 32: 802.11 – DCF with RTS/CTS
Sending unicast packets
  station can send RTS with reservation parameter after waiting for DIFS (reservation determines amount of time the data packet needs the medium)
  acknowledgement via CTS after SIFS by receiver (if ready to receive)
  sender can now send data at once, acknowledgement via ACK
  other stations store medium reservations distributed via RTS and CTS
t
SIFS
DIFS
data
ACK
defer access
other
stations
receiver
sender
data
DIFS
contention
RTS
CTS
SIFS
SIFS
NAV (RTS)
NAV (CTS)

## Slide 33: Fragmentation
t
SIFS
DIFS
data
ACK1
other
stations
receiver
sender
frag1
DIFS
contention
RTS
CTS
SIFS
SIFS
NAV (RTS)
NAV (CTS)
NAV (frag1)
NAV (ACK1)
SIFS
ACK2
frag2
SIFS

## Slide 34: 802.11 – MAC Frame format
Types
  control frames, management frames, data frames
Sequence numbers
  important against duplicated frames due to lost ACKs
Addresses
  receiver, transmitter (physical), BSS identifier, sender (logical)
Miscellaneous
  sending time, checksum, frame control, data
Frame
Control
Duration/
ID
Address
1
Address
2
Address
3
Sequence
Control
Address
4
Frame
Body
FCS
2
2
6
6
6
6
2
4
0-7951
bytes
Protocol
version
Type
Subtype
To
DS
More
Frag
Retry
Power
Mgmt
More
Data
Protec-
ted
Frame
2
2
4
1
From
DS
1
+HTC/
Order
bits
1
1
1
1
1
1
QoS
Control
2
HT
Control
4
Only the first three and the last field are present in all frames!

## Slide 35: MAC address format (examples)
AP: Access Point
DA: Destination Address
SA: Source Address
BSSID: Basic Service Set Identifier
RA: Receiver Address
TA: Transmitter Address

## Slide 36: Special Frames: ACK, RTS, CTS
Acknowledgement
Request To Send
Clear To Send
Frame
Control
Duration
Receiver
Address
Transmitter
Address
FCS
2
2
6
6
4
bytes
Frame
Control
Duration
Receiver
Address
FCS
2
2
6
4
bytes
Frame
Control
Duration
Receiver
Address
FCS
2
2
6
4
bytes
ACK
RTS
CTS

## Slide 37: Questions & Tasks
  Why is it difficult to guarantee QoS at MAC layer?
  How does 802.11 prioritize different packets?
  What is the behavior of the basic access method under no/light/heavy load?
  How is fairness implemented?
  Why is the contention window mechanism unfair?
  What is the idea of the NAV?
  How is the problem with hidden/exposed stations solved?

## Slide 38: 802.11 - MAC management
Synchronization
  try to find a LAN, try to stay within a LAN
  timer etc.
Power management
  sleep-mode without missing a message
  periodic sleep, frame buffering, traffic measurements
Association/Reassociation
  integration into a LAN
  roaming, i.e. change networks by changing access points
  scanning, i.e. active search for a network
MIB - Management Information Base
  managing, read, write

## Slide 39: Synchronization using a Beacon (infrastructure)
beacon interval
(20ms – 1s)
t
medium
access
point
busy
B
busy
busy
busy
B
B
B
value of the timestamp
B
beacon frame

## Slide 40: Synchronization using a Beacon (ad-hoc)
t
medium
station1
busy
B1
beacon interval
busy
busy
busy
B1
value of the timestamp
B
beacon frame
station2
B2
B2
random delay

## Slide 41: Power management
Idea: switch the transceiver off if not needed
  States of a station: sleep and awake
Timing Synchronization Function (TSF)
  stations wake up at the same time
Infrastructure
  Traffic Indication Map (TIM)
    list of unicast receivers transmitted by AP
  Delivery Traffic Indication Map (DTIM)
    list of broadcast/multicast receivers transmitted by AP
Ad-hoc
  Ad-hoc Traffic Indication Map (ATIM)
    announcement of receivers by stations buffering frames
    more complicated - no central AP
    collision of ATIMs possible (scalability?)
APSD (Automatic Power Save Delivery)
  more efficient method in 802.11e replacing above schemes offering scheduled (S-APSD) and unscheduled service periods (U-APSD)

## Slide 42: Power saving with wake-up patterns (infrastructure)
TIM interval
t
medium
access
point
busy
D
busy
busy
busy
T
T
D
T
TIM
D
DTIM
DTIM interval
B
B
B
broadcast/multicast
station
awake
p
PS poll
p
d
d
d
data transmission
to/from the station

## Slide 43: U-APSD – WMM Power Save
Procedure for unicast data delivered to a STA in PS mode
STA triggers release of buffered data from AP
WMM Power Save based on legacy procedures plus optional U-APSD
Advantages:
  No more polling needed
  Downlink data frames sent together in a fast sequence
  Trigger frame may already contain data – ideal e.g. for VoIP
  Applications specify PS behavior, i.e. sleep period
STA
AP
ACK
data / null
awake
data / null
ACK
data / null
ACK
no more than max. service period length

## Slide 44: 802.11 - Roaming
No or bad connection? Then perform:
Scanning
  scan the environment, i.e., listen into the medium for beacon signals or send probes into the medium and wait for an answer
Reassociation Request
  station sends a request to one or several AP(s)
Reassociation Response
  success: AP has answered, station can now participate
  failure: continue scanning
AP accepts Reassociation Request
  signal the new station to the distribution system
  the distribution system updates its data base (i.e., location information)
  typically, the distribution system now informs the old AP so it can release resources
May take a long time …

## Slide 45: Faster roaming using 802.11k, .11r and .11v
Classical roaming is too slow, e.g., for VoIP over WLAN  service interruption
  802.11 authentication message exchange
  Reassociation messages exchange
  EAP-request/response identity exchange
  Access request and challenge packet exchange
  EAP request/response
  RADIUS access request/accept exchange
  Success message to Client
  Nonce-value exchange
  Temporal key, acknowledgement exchange
In this example 17 steps (all but 7. are exchanges)!
  See 802.1X for more details about authentication
802.11k: Optimized channel list
  Collect potential roaming networks prior to roaming
802.11r: Fast BSS Transition - only 4 steps left
  Client and AP exchange 802.11 authentication messages and nonce-values
  Client and AP exchange reassociation messages and temporal key/acknowledgment
802.11v: BSS Transition Management
  Manage information about alternative access points
  Disassociation Imminent can force client to roam

## Slide 46: WLAN: IEEE 802.11 – some developments
802.11c: Bridge Support
  Definition of MAC procedures to support bridges as extension to 802.1D
802.11d: Regulatory Domain Update
  Support of additional regulations related to channel selection, hopping sequences
802.11e: MAC Enhancements – QoS
  Enhance the current 802.11 MAC to expand support for applications with Quality of Service requirements, and in the capabilities and efficiency of the protocol
  Definition of a data flow (“connection”) with parameters like rate, burst, period… supported by HCCA (HCF (Hybrid Coordinator Function) Controlled Channel Access, optional)
  Additional energy saving mechanisms and more efficient retransmission
  EDCA (Enhanced Distributed Channel Access): high priority traffic waits less for channel access
802.11F: Inter-Access Point Protocol (withdrawn)
  Establish an Inter-Access Point Protocol for data exchange via the distribution system
802.11g: Data Rates > 20 Mbit/s at 2.4 GHz; 54 Mbit/s, OFDM
  Successful successor of 802.11b, performance loss during mixed operation with .11b
802.11h: Spectrum Managed 802.11a
  Extension for operation of 802.11a in Europe by mechanisms like channel measurement for dynamic channel selection (DFS, Dynamic Frequency Selection) and power control (TPC, Transmit Power Control)
802.11i: Enhanced Security Mechanisms
  Enhance the current 802.11 MAC to provide improvements in security.
  TKIP enhances the insecure WEP, but remains compatible to older WEP systems
  AES provides a secure encryption method and is based on new hardware

## Slide 47: WLAN: IEEE 802.11 – some developments
802.11j: Extensions for operations in Japan
  Changes of 802.11a for operation at 5GHz in Japan using only half the channel width at larger range
802.11k: Methods for channel measurements
  Devices and access points should be able to estimate channel quality in order to be able to choose a better access point of channel
802.11m: Updates of the 802.11-2007 standard
802.11n: Higher data rates above 100Mbit/s
  Changes of PHY and MAC with the goal of 100Mbit/s at MAC SAP
  MIMO antennas (Multiple Input Multiple Output), up to 600Mbit/s are currently feasible
  However, still a large overhead due to protocol headers and inefficient mechanisms
802.11p: Inter car communications
  Communication between cars/road side and cars/cars
  Planned for relative speeds of min. 200km/h and ranges over 1000m
  Usage of 5.850-5.925GHz band in North America
802.11r: Faster Handover between BSS (“roaming”)
  Secure, fast handover of a station from one AP to another within an ESS
  Current mechanisms (even newer standards like 802.11i) plus incompatible devices from different vendors are massive problems for the use of, e.g., VoIP in WLANs
  Handover should be feasible within 50ms in order to support multimedia applications efficiently
802.11s: Mesh Networking
  Design of a self-configuring Wireless Distribution System (WDS) based on 802.11
  Support of point-to-point and broadcast communication across several hops

## Slide 48: WLAN: IEEE 802.11 – some developments
802.11T: Performance evaluation of 802.11 networks
  Standardization of performance measurement schemes
802.11u: Interworking with additional external networks
802.11v: Network management
  Extensions of current management functions, channel measurements
  Definition of a unified interface
802.11w: Securing of network control
  Classical standards like 802.11, but also 802.11i protect only data frames, not the control frames. Thus, this standard should extend 802.11i in a way that, e.g., no control frames can be forged.
802.11y: Extensions for the 3650-3700 MHz band in the USA
802.11z: Extension to direct link setup
802.11aa: Robust audio/video stream transport
802.11ac: Very High Throughput <6Ghz – up to almost 7 Gbit/s @ 5GHz using 8x8 MIMO
802.11ad: Very High Throughput in 60 GHz
802.11af: TV white space, ah: sub 1GHz, ai: fast initial link set-up; … aq: pre-association discovery,
802.11ax: High Efficiency Wireless LAN (HEW)
802.11ay: Next Generation 60 GHz (NG60), az: Next Generation Positioning (NGP), ba: Wake-up radio, bb: light, …
802.11-2016: Current “complete” standard - 3534 pages!
  Comprises many amendments
Note: Not all “standards” will end in products, many ideas get stuck at working group level
Info: www.ieee802.org/11/; dig into Task Group Meetings

## Slide 49: Current top standard IEEE 802.11ax – High Efficiency WLAN – marketed as WiFi 6(E)
Increased number of non-overlapping channels at 6 GHz

## Slide 50: Improvements of 802.11ax over 802.11ac
  Centrally (AP) controlled MAC with dynamic bandwidth assignment using OFDMA via Resource Units (RU, time-frequency resources, see LTE!)
  Multi-user MIMO in up- and downlink, AP sends trigger with scheduling information (modulation, coding, RUs)
  Mix of assigned and random access RUs for uplinks
  Spatial frequency reuse via “coloring” of signals (distinguishes own/neighboring network) plus adaptive power/sensitivity thresholds
  Two NAVs: own network and overlapping network to avoid misbehavior
  Dynamic fragmentation helps reducing overhead (fill available RUs)
  Longer guard intervals for better protection against signal delay spread (outdoor conditions)

## Slide 51: Data rates for 802.11ax
  Values are for a single spatial stream
  Depending on number of streams devices with > 10 Gbit/s available
MCS | Modulation | Coding rate | Data rate in Mbit/s per spatial stream |  |  |  |  |  |  | 
 |  |  | 20 MHz channels |  | 40 MHz channels |  | 80 MHz channels |  | 160 MHz channels | 
 |  |  | 1600 ns GI | 800 ns GI | 1600 ns GI | 800 ns GI | 1600 ns GI | 800 ns GI | 1600 ns GI | 800 ns GI
0 | BPSK | 1/2 | 8 | 8.6 | 16 | 17.2 | 34 | 36.0 | 68 | 72
1 | QPSK | 1/2 | 16 | 17.2 | 33 | 34.4 | 68 | 72.1 | 136 | 144
2 | QPSK | 3/4 | 24 | 25.8 | 49 | 51.6 | 102 | 108.1 | 204 | 216
3 | 16-QAM | 1/2 | 33 | 34.4 | 65 | 68.8 | 136 | 144.1 | 272 | 282
4 | 16-QAM | 3/4 | 49 | 51.6 | 98 | 103.2 | 204 | 216.2 | 408 | 432
5 | 64-QAM | 2/3 | 65 | 68.8 | 130 | 137.6 | 272 | 288.2 | 544 | 576
6 | 64-QAM | 3/4 | 73 | 77.4 | 146 | 154.9 | 306 | 324.4 | 613 | 649
7 | 64-QAM | 5/6 | 81 | 86.0 | 163 | 172.1 | 340 | 360.3 | 681 | 721
8 | 256-QAM | 3/4 | 98 | 103.2 | 195 | 206.5 | 408 | 432.4 | 817 | 865
9 | 256-QAM | 5/6 | 108 | 114.7 | 217 | 229.4 | 453 | 480.4 | 907 | 961
10 | 1024-QAM | 3/4 | 122 | 129.0 | 244 | 258.1 | 510 | 540.4 | 1021 | 1081
11 | 1024-QAM | 5/6 | 135 | 143.4 | 271 | 286.8 | 567 | 600.5 | 1134 | 1201

## Slide 52: Questions & Tasks
  Check the differences between WiFi, WMM, … and the 802.11 standard!
  Why is synchronization needed?
  What are the negative effects of the power saving mechanisms, what are the trade-offs between power consumption and transmission QoS? What is the advantage of U-APSD?
  Why can roaming consume a lot of time? How to speed-up the process?
  What is left from the distributed WLAN mechanisms when looking at the most current standards?

## Slide 53: Bluetooth
Basic idea long time ago
  Universal radio interface for ad-hoc wireless connectivity
  Interconnecting computer and peripherals, handheld devices, PDAs, cell phones – replacement of IrDA
  Embedded in other devices, goal: 5€/device (pretty soon < 1€)
  Short range (10 m), low power consumption, license-free 2.45 GHz ISM band
  Voice and data transmission, approx. 1 Mbit/s gross data rate
One of the first modules (Ericsson).

## Slide 54: Bluetooth
History
  1994: Ericsson (Mattison/Haartsen), “MC-link” project
  Renaming of the project: Bluetooth according to Harald “Blåtand” Gormsen [son of Gorm], King of Denmark in the 10th century
  1998: foundation of Bluetooth SIG, www.bluetooth.org
  1999: erection of a rune stone at Ercisson/Lund ;-)
  2001: first consumer products for mass market, spec. version 1.1 released
  2005: 5 million chips/week
Special Interest Group
  Original founding members: Ericsson, Intel, IBM, Nokia, Toshiba
  Added promoters: 3Com, Agere (was: Lucent), Microsoft, Motorola
  > 10000 members
  Common specification and certification of products
  2020: core specification 5.2 comprises 3256 pages!
(was: )

## Slide 55: History and hi-tech…
1999:
Ericsson mobile communications AB reste denna sten till minne av Harald Blåtand, som fick ge sitt namn åt en ny teknologi för trådlös, mobil kommunikation.

## Slide 56: …and the real rune stone
Located in Jelling, Denmark,
erected by King Harald “Blåtand”
in memory of his parents.
The stone has three sides – one side
showing a picture of Christ.
This could be the “original” colors of the stone.
Inscription:
“auk tani karthi kristna” (and made the Danes Christians)
Inscription:
"Harald king executes these sepulchral monuments after Gorm, his father and Thyra, his mother. The Harald who won the whole of Denmark and Norway and turned the Danes to Christianity."
Btw: Blåtand has nothing to do
with a blue tooth…

## Slide 57: Bluetooth today - Overview
Basic Rate (BR) – up to 723.2 kbit/s
  Optional EDR (Enhanced Data Rate, 2.1 Mbit/s ), AMP (Alternate MAC and PHY, 54 Mbit/s)
  Headsets, keyboards, …
Low Energy (LE) – up to 2 Mbit/s
  Lower power, cost, complexity, duty cycles
  Smart beacons, home automation, …
Source: www.Bluetooth.org, BT_Core, v5.2

## Slide 58: Characteristics of the classical system – Bluetooth BR
2.4 GHz ISM band, 79 RF channels, 1 MHz carrier spacing
  Channel 0: 2402 MHz … channel 78: 2480 MHz
  GFSK modulation, 1-100 mW transmit power
FHSS and TDD
  Frequency hopping with 1600 hops/s
  Hopping sequence in a pseudo random fashion, determined by a master
  Time division duplex for send/receive separation
Voice link – SCO (Synchronous Connection Oriented)
  FEC (forward error correction), no retransmission, 64 kbit/s duplex, point-to-point, circuit switched
Data link – ACL (Asynchronous ConnectionLess)
  Asynchronous, fast acknowledge, point-to-multipoint, up to 433.9 kbit/s symmetric or 723.2/57.6 kbit/s asymmetric, packet switched
Topology
  Overlapping piconets (stars) forming a scatternet

## Slide 59: Piconet
Collection of devices connected in an ad hoc fashion
One unit acts as master and the others as slaves for the lifetime of the piconet
Master determines hopping pattern, slaves have to synchronize
Each piconet has a unique hopping pattern
Participation in a piconet = synchronization to hopping sequence
Each piconet has one master and up to 7 simultaneous slaves
M=Master
S=Slave
SB=Standby
M
S
SB
S
S
SB

## Slide 60: Forming a piconet
All devices in a piconet hop together
  Master gives slaves its clock and device ID
    Hopping pattern: determined by device ID (48 bit, unique worldwide)
    Phase in hopping pattern determined by clock
Addressing
  Logical Transport Address (LT_ADDR, 3 bit)
SB
SB
SB
SB
SB
SB
SB
SB
SB
M
S
SB
SB
S
S
SB
SB
SB



















## Slide 61: Scatternet
Linking of multiple co-located piconets through the sharing of common master or slave devices
  Devices can be slave in one piconet and master of another
Communication between piconets
  Devices jumping back and forth between the piconets
M=Master
S=Slave
SB=Standby
M
S
SB
S
S
SB
M
S
S
SB
Piconets
(each with a
capacity of
720 kbit/s)

## Slide 62: Bluetooth protocol stack – classical view
Radio
Baseband
Link Manager
Control
Host
Controller
Interface
Logical Link Control and Adaptation Protocol (L2CAP)
Audio
TCS BIN
SDP
OBEX
vCal/vCard
IP
NW apps.
TCP/UDP
BNEP
RFCOMM (serial line interface)
AT modem
commands
telephony apps.
audio apps.
mgmnt. apps.
AT: attention sequence
OBEX: object exchange
TCS BIN: telephony control protocol specification – binary
BNEP: Bluetooth network encapsulation protocol
SDP: service discovery protocol
RFCOMM: radio frequency comm.
PPP

## Slide 63: Frequency selection during data transmission
S
fk
625 µs
fk+1
fk+2
fk+3
fk+4
fk+3
fk+4
fk
fk
fk+5
fk+5
fk+1
fk+6
fk+6
fk+6
M
M
M
M
M
M
M
M
M
t
t
t
S
S
S
S
S

## Slide 64: Baseband
Piconet/channel definition
Low-level packet definition
  Access code
    Channel, device access, e.g., derived from master
  Packet header
    1/3-FEC, Logical Transport Address (broadcast + 7 slaves), link type, alternating bit ARQ/SEQ, checksum
access code
packet header
payload
68(72)
54
0-2745
bits
LT_ADDR
type
flow
ARQN
SEQN
HEC
3
4
1
1
1
8
bits
preamble
sync.
(trailer)
4
64
(4)
Guard/sync
(EDR only)
PHY channel access
Logical transport identifier
EDR PHY mode change (GFSK to DPSK)

## Slide 65: Classical SCO payload types
payload (30)
audio (30)
audio (10)
audio (10)
HV3
HV2
HV1
DV
FEC (20)
audio (20)
FEC (10)
header (1)
payload (0-9)
2/3 FEC
CRC (2)
(bytes)

## Slide 66: Classical ACL Payload types
payload (0-343)
header (1/2)
payload (0-339)
CRC (2)
header (1)
payload (0-17)
2/3 FEC
header (1)
payload (0-27)
header (2)
payload (0-121)
2/3 FEC
header (2)
payload (0-183)
header (2)
payload (0-224)
2/3 FEC
header (2)
payload (0-339)
DH5
DM5
DH3
DM3
DH1
DM1
header (1)
payload (0-29)
AUX1
CRC (2)
CRC (2)
CRC (2)
CRC (2)
CRC (2)
CRC (2)
(bytes)

## Slide 67: Baseband data rates (examples)
ACL packets
SCO packets
Source: www.Bluetooth.org, BT_Core

## Slide 68: Questions & Tasks
  What were in the beginning, what are today the goals of Bluetooth?
  What are basic differences between WLAN and Bluetooth BR/EDR?
  What is a piconet?
  Why is there no collision in a piconet? How can collisions occur?
  How does EDR achieve higher data rates?

## Slide 69: Baseband link types
Polling-based TDD packet transmission
  625µs slots, master polls slaves
SCO (Synchronous Connection Oriented) – Voice
  Periodic single slot packet assignment, 64 kbit/s full-duplex, point-to-point
ACL (Asynchronous ConnectionLess) – Data
  Variable packet size (1, 3, 5 slots), asymmetric bandwidth, point-to-multipoint
MASTER
SLAVE 1
SLAVE 2
f6
f0
f1
f7
f12
f13
f19
f18
SCO
SCO
SCO
SCO
ACL
f5
f21
f4
f20
ACL
ACL
f8
f9
f17
f14
ACL

## Slide 70: Robustness
Slow frequency hopping with hopping patterns determined by a master
  Protection from interference on certain frequencies
  Separation from other piconets (FH-CDMA)
Retransmission
  ACL only, very fast
Forward Error Correction
  SCO and ACL
MASTER
SLAVE 1
SLAVE 2
A
C
C
H
F
G
G
B
D
E
NAK
ACK
Error in payload
(not header!)

## Slide 71: Baseband states of a Bluetooth device
standby
inquiry
page
connected
transmit
hold
sniff
unconnected
connecting
active
low power
Standby: do nothing
Inquire: search for other devices
Page: connect to a specific device
Connected: participate in a piconet
detach
Sniff: listen periodically, not each slot
Hold: stop ACL, SCO still possible, possibly participate in another piconet
Some more defined: role swapping, EDR, …

## Slide 72: Classical Example: Power consumption/CSR BlueCore2
Typical Average Current Consumption1
  VDD=1.8V Temperature = 20°C
  Mode
    SCO connection HV3 (1s interval Sniff Mode) (Slave) 26.0 mA
    SCO connection HV3 (1s interval Sniff Mode) (Master) 26.0 mA
    SCO connection HV1 (Slave) 53.0 mA
    SCO connection HV1 (Master) 53.0 mA
    ACL data transfer 115.2kbps UART (Master) 15.5 mA
    ACL data transfer 720kbps USB (Slave) 53.0 mA
    ACL data transfer 720kbps USB (Master) 53.0 mA
    ACL connection, Sniff Mode 40ms interval, 38.4kbps UART 4.0 mA
    ACL connection, Sniff Mode 1.28s interval, 38.4kbps UART 0.5 mA
    Parked Slave, 1.28s beacon interval, 38.4kbps UART 0.6 mA
    Standby Mode (Connected to host, no RF activity) 47.0 µA
    Deep Sleep Mode2 20.0 µA
Notes:
  1 Current consumption is the sum of both BC212015A and the flash.
  2 Current consumption is for the BC212015A device only.

## Slide 73: Example: Bluetooth/USB adapter (2002: 50€, today: some cents if integrated)

## Slide 74: L2CAP - Logical Link Control and Adaptation Protocol
Simple data link protocol on top of baseband
Connection oriented, connectionless, and signaling channels
Protocol multiplexing
  RFCOMM, SDP, telephony control
Segmentation & reassembly
  Up to 64kbyte user data, 16 bit CRC used from baseband
QoS flow specification per channel
  Follows RFC 1363, specifies delay, jitter, bursts, bandwidth
Group abstraction
  Create/close group, add/remove member

## Slide 75: L2CAP logical channels
baseband
L2CAP
baseband
L2CAP
baseband
L2CAP
Slave
Slave
Master
ACL
2
d
1
d
d
1
1
d
2
1
signalling
connectionless
connection-oriented
d
d
d

## Slide 76: L2CAP packet formats
length
2
bytes
CID=2
2
PSM
2
payload
0-65533
length
2
bytes
CID
2
payload
0-65535
length
2
bytes
CID=1
2
One or more commands
Connectionless PDU
Connection-oriented PDU
Signalling command PDU
code
ID
length
data
1
1
2
0

## Slide 77: Security - simplified
E3
E2
link key (128 bit)
encryption key (128 bit)
payload key
Keystream generator
Data
Data
Cipher data
Authentication key generation
(possibly permanent storage)
Encryption key generation
(temporary storage)
PIN (1-16 byte)
User input (initialization)
Pairing
Authentication
Encryption
Ciphering
E3
E2
link key (128 bit)
encryption key (128 bit)
payload key
Keystream generator
PIN (1-16 byte)
newer:
numeric comparison
just works
out-of-band
passkey entry

## Slide 78: SDP – Service Discovery Protocol
Inquiry/response protocol for discovering services
  Searching for and browsing services in radio proximity
  Adapted to the highly dynamic environment
  Can be complemented by others like SLP, Jini, Salutation, …
  Defines discovery only, not the usage of services
  Caching of discovered services
  Gradual discovery
Service record format
  Information about services provided by attributes
  Attributes are composed of an 16 bit ID (name) and a value
  values may be derived from 128 bit Universally Unique Identifiers (UUID)

## Slide 79: Additional protocols to support legacy protocols/apps.
RFCOMM
  Emulation of a serial port (supports a large base of legacy applications)
  Allows multiple ports over a single physical channel
Telephony Control Protocol Specification (TCS)
  Call control (setup, release)
  Group management
OBEX
  Exchange of objects, IrDA replacement
WAP
  Interacting with applications on cellular phones

## Slide 80: Profiles
Represent default solutions for a certain usage model
  Vertical slice through the protocol stack
  Basis for interoperability
  Defines options and parameters
Examples
  A2DP: Advanced Audio Distribution Profile
  BIP: Basic Imaging Profile
  CTN: Calendar Tasks and Notes Profile
  FTP: File Transfer Profile
  GNSS: Global Navigation Satellite System Profile
  HDP: Health Device Profile
  HID: Human Interface Device Profile
  PBAP: Phone Book Access Profile
  SPP: Serial Port Profile
  … see https://www.bluetooth.com/specifications/profiles-overview/
Profiles
Protocols
Applications

## Slide 81: Questions & Tasks
  How does Bluetooth guarantee certain data rates and delays?
  Can slaves send on their own?
  How can the sniff mode help reducing power consumption?
  If interested in the current security features – please do have a look at the Core Spec!
  Many protocols, options, parameters – quite complex! What is one offered solution to guarantee compatibility?

## Slide 82: Bluetooth versions
Bluetooth 1.1
  also IEEE Standard 802.15.1-2002
  initial stable commercial standard
Bluetooth 1.2
  also IEEE Standard 802.15.1-2005
  eSCO (extended SCO): higher, variable bitrates, retransmission for SCO
  AFH (adaptive frequency hopping) to avoid interference
Bluetooth 2.0 + EDR (2004, no more IEEE)
  EDR (enhanced date rate) of 3.0 Mbit/s for ACL and eSCO
  lower power consumption due to shorter duty cycle
Bluetooth 2.1 + EDR (2007)
  better pairing support, e.g. using NFC
  improved security
Bluetooth 3.0 + HS (2009)
  Bluetooth 2.1 + EDR + IEEE 802.11a/g = 54 Mbit/s
Bluetooth 4.0 (2010), 4.1 (2013), 4.2 (2014)
  Low Energy, much faster connection setup
Bluetooth 5 (2016)
  Longer range (100m) or higher data rate (2 Mbit/s without EDR), localization, no more park state

## Slide 83: Bluetooth Low Energy – this is not classical BT anymore!
Also at 2.4 GHz, FHSS, mandatory 1 Mbit/s, 500 kbit/s, 125 kbit/s as well as optional 2 Mbit/s
Special mesh networking for many-to-many communication between thousands of devices
Two MAC schemes
  FDMA
    40 channels, 2 MHz spacing, 3 channels for advertising, 37 general purpose (advertising, data)
  TDMA
    Polling scheme with predetermined intervals
Physical channel sub-divided into “events”
  Advertising, extended advertising, periodic advertising, connection, isochronous
Radio supports direction finding (angle of arrival / departure) useful for RTLS
Source: www.nordicsemi.com, nRF5340

## Slide 84: BLE Physical Channels
Source: www.Bluetooth.org, BT_Core, v5.2

## Slide 85: BLE Packet Format – Example: Uncoded PHY LE 1M and LE 2M)
Preamble
  Synchronization, gain control, symbol timing
  1 byte for LE 1M, 2 byte for LE 2M
Access Address
  Determined by the link layer
Constant Tone Extension
  Optional for AoA/AoD estimation
Source: www.Bluetooth.org, BT_Core, v5.2

## Slide 86: BLE Advertisements
  Communication can happen in advertising events
  Each advertising event starts at the first advertising channel k
  Advertisers send advertisements, scanners receive and may make a request answered by the advertiser
  Advertisements can be used to set-up bidirectional communication, periodic broadcasts, isochronous streams
Source: www.Bluetooth.org, BT_Core, v5.2

## Slide 87: BLE setting up ACL connections
  Devices (called initiator) may listen for connectable advertising packets
  After reception the initiator may make a connection request on the same channel
  Start of connecting event if advertiser accepts connection request
  Initiator becomes master in the piconet, advertising device the slave
  Channel hopping at each connection event based on hopping pattern determined by connection request
    Pseudo-random pattern using 37 frequencies incl. interference prevention via exclusion of channels
  Using an ACL connection the master can establish one or more isochronous connections
Source: www.Bluetooth.org, BT_Core, v5.2

## Slide 88: Example Roles and Topologies
Piconet A
  A is master
  B is slave
  C is slave
  BUT: slaves do NOT share same frequencies!
Group D
  D is advertiser
  A is initiator
  A could add D to piconet A
Group C
  C is advertiser
  E is scanner
Advertisements may happen on different advertising channels to avoid collisions
A
B
D
C
E
Piconet A
Group D
Group C

## Slide 89: Link Layer State Diagram
Source: www.Bluetooth.org, BT_Core, v5.2

## Slide 90: Questions & Tasks
  What are major changes when going from Bluetooth BR/EDR to Bluetooth LE?
  How do devices “find” each other?
  What are differences of BT BR/EDR piconets and BT LE piconets?
  Why can BT LE devices react/transmit faster?
  Where can collisions happen during data transmission?

## Slide 91: WPAN: IEEE 802.15 – additional developments 1
802.15.2: Coexistance
  Coexistence of Wireless Personal Area Networks (802.15) and Wireless Local Area Networks (802.11), quantify the mutual interference
802.15.3: High-Rate
  Standard for high-rate (20Mbit/s or greater) WPANs, while still low-power/low-cost
  Data Rates: 11, 22, 33, 44, 55 Mbit/s
  Quality of Service isochronous protocol
  Ad hoc peer-to-peer networking
  Security
  Low power consumption
  Low cost
  Designed to meet the demanding requirements of portable consumer imaging and multimedia applications

## Slide 92: WPAN: IEEE 802.15 – additional developments 2
Several working groups extend the 802.15.3 standard
802.15.3a: - withdrawn -
  Alternative PHY with higher data rate as extension to 802.15.3
  Applications: multimedia, picture transmission
802.15.3b:
  Enhanced interoperability of MAC
  Correction of errors and ambiguities in the standard
802.15.3c:
  Alternative PHY at 57-64 GHz
  Goal: data rates above 2 Gbit/s
Not all these working groups really create a standard, not all standards will be found in products later …

## Slide 93: WPAN: IEEE 802.15 – additional developments 3
802.15.4: Low-Rate, Very Low-Power
  Low data rate solution with multi-month to multi-year battery life and very low complexity
  Potential applications are sensors, interactive toys, smart badges, remote controls, and home automation
  Data rates of 20-250 kbit/s, latency down to 15 ms
  Master-Slave or Peer-to-Peer operation
  Up to 254 devices or 64516 simpler nodes
  Support for critical latency devices, such as joysticks
  CSMA/CA channel access (data centric), slotted (beacon) or unslotted
  Automatic network establishment by the PAN coordinator
  Dynamic device addressing, flexible addressing format
  Fully handshaked protocol for transfer reliability
  Power management to ensure low power consumption
  16 channels in the 2.4 GHz ISM band, 10 channels in the 915 MHz US ISM band and one channel in the European 868 MHz band
Base of the ZigBee technology – www.zigbee.org

## Slide 94: Zigbee
Relation to 802.15.4 similar to Bluetooth / 802.15.1
Pushed by Chipcon (now TI), ember, freescale (Motorola), Honeywell, Mitsubishi, Motorola, Philips, Samsung…
More than 260 members – see www.zigbee.org
  about 19 promoters, 133 participants, 162 adopters
  must be member to commercially use ZigBee spec
ZigBee platforms comprise
  IEEE 802.15.4 for layers 1 and 2
  ZigBee protocol stack up to the applications

## Slide 95: Zigbee Technical Specifications
Source: www.zigbeealliance.org

## Slide 96: Zigbee Network Topology Example – Centralized Security
  Mesh, self-organizing, self-healing topology scalable to thousands of nodes
  Interference tolerance via clear channel assessments, retries, etc.
  Point to Point communication gives range > 100 m; full mesh deployment can have several kilometer range
  End device
    Single parent, no routing
    Often battery powered
  Router
  Coordinator
    Owns the network
  FFD (Full Function Device)
    Mains powered, can route, always on
  RFD (Reduced Function Device)
    Talks only to parent, can sleep
Source: www.zigbeealliance.org
Zigbee End Device (RFD or FFD)
Zigbee Router (FFD)
Zigbee Coordinator (FFD)
Bi-directional Mesh Link

## Slide 97: WPAN: IEEE 802.15 – additional developments 4
802.15.4a:
  Alternative PHY with lower data rate as extension to 802.15.4
  Properties: precise localization (< 1m precision), extremely low power consumption, longer range
  Two PHY alternatives
    UWB (Ultra Wideband): ultra short pulses, communication and localization
    CSS (Chirp Spread Spectrum): communication only
802.15.4b, c, d, e, f, g, … r, s:
  Extensions, corrections, and clarifications regarding 802.15.4
  Usage of new bands, more flexible security mechanisms
  RFID, smart utility neighborhood (high scalability)
802.15.5: Mesh Networking
  Partial meshes, full meshes
  Range extension, more robustness, longer battery live
802.15.6: Body Area Networks
  Low power networks e.g. for medical or entertainment use
802.15.7: Visible Light Communication ……………. and many, many more!
Not all these working groups really create a standard, not all standards will be found in products later … see http://www.ieee802.org/15/

## Slide 98: Some more IEEE standards for mobile communications
IEEE 802.16: Broadband Wireless Access / WirelessMAN / WiMax – hibernating (dead due to LTE…)
  Wireless distribution system, e.g., for the last mile, alternative to DSL
  75 Mbit/s up to 50 km LOS, up to 10 km NLOS; 2-66 GHz band
  Initial standards without roaming or mobility support
  802.16e adds mobility support, allows for roaming at 150 km/h
IEEE 802.19: Wireless Coexistence Working Group
  Standards for the coexistence between wireless standards of unlicensed devices
IEEE 802.20: Mobile Broadband Wireless Access (MBWA) Working Group - disbanded
IEEE 802.21: Media Independent Handover Interoperability - hibernating
  Standardize handover between different 802.x and/or non 802 networks
IEEE 802.22: Wireless Regional Area Networks (WRAN) - hibernating
  Radio-based PHY/MAC for use by license-exempt devices on a non-interfering basis in spectrum that is allocated to the TV Broadcast Service

## Slide 99: RF Controllers – ISM bands
Data rate
  Typ. up to 115 kbit/s (serial interface)
Transmission range
  5-100 m, depending on power (typ. 10-500 mW)
Frequency
  Typ. 27 (EU, US), 315 (US), 418 (EU), 426 (Japan), 433 (EU), 868 (EU), 915 (US) MHz (depending on regulations)
Security
  Some products with added processors
Cost
  Cheap: 10€-50€
Availability
  Many products, many vendors
Connection set-up time
  N/A
Quality of Service
  none
Manageability
  Very simple, same as serial interface
Special Advantages/Disadvantages
  Advantage: very low cost, large experience, high volume available
  Disadvantage: no QoS, crowded ISM bands (particularly 27 and 433 MHz), typ. no Medium Access Control, 418 MHz experiences interference with TETRA

## Slide 100: ISM band interference
Many sources of interference
  Microwave ovens, microwave lighting
  802.11, 802.11b, 802.11g, 802.15, …
  Even old analog TV transmission, surveillance
  Unlicensed metropolitan area networks
  …
Levels of interference
  Physical layer: interference acts like noise
    Spread spectrum tries to minimize this
    FEC/interleaving tries to correct
  MAC layer: algorithms not harmonized
    E.g., Bluetooth might confuse 802.11
OLD
© Fusion Lighting, Inc., now used by LG as Plasma Lighting System
NEW

## Slide 101: 802.11 vs.(?) 802.15/Bluetooth – a problem from the beginning?
Bluetooth may act like a rogue member of the 802.11 network
  Does not know anything about gaps, inter frame spacing etc.
IEEE 802.15-2 discusses these problems
  Proposal: Adaptive Frequency Hopping
    a non-collaborative Coexistence Mechanism
Real effects? Many different opinions, publications, tests, formulae, …
  Results from complete breakdown to almost no effect
  Bluetooth (FHSS) seems more robust than 802.11b (DSSS)
t
f [MHz]
2402
2480
802.11b
3 channels
(separated by installation)
ACK
DIFS
DIFS
SIFS
1000 byte
SIFS
DIFS
500 byte
ACK
DIFS
500 byte
SIFS
ACK
DIFS
500 byte
DIFS
100
byte
SIFS
ACK
DIFS
100
byte
SIFS
ACK
DIFS
100
byte
SIFS
ACK
DIFS
100
byte
SIFS
ACK
DIFS
100
byte
SIFS
ACK
802.15.1
79 channels
(separated by hopping pattern)

## Slide 102: Overview – who is where?
Bluetooth BR/EDR
Bluetooth LE
ZigBee 802.15.4
WLAN 802.11
Source: S. Raza

## Slide 103: Mechanisms for Interference avoidance in the ISM band – Example Bluetooth
Adaptive Frequency Hopping
  Reduce the number of channels used in a piconet (min. 20 out of 79)
HCI Set Host Channel Classification
  Host informs BT controller of the occupied channels by e.g. WLAN
Enhanced SCO
  Added retransmissions to SCO
Piconet Clock Adjust
  Align clock with external technology
Slot Availability Mask
  Exchange available time slot
…

## Slide 104: Questions & Tasks
  Check the additional developments yourself – several “overlapping” goals and competing standards!
  What is the main purpose of Zigbee?
  What are key characteristics of Zigbee networks? Differences to Bluetooth (LE)?
  How can wireless systems avoid interference? What does Bluetooth offer?