## Slide 1: Mobile Communications Chapter 6: Internet Protocols
Mobile IP, Security, MIPv6, PMIPv6
Micro mobility support, Locator/ID split
Ad-hoc networks, Routing protocols, WSN/IoT
TCP-mechanisms
Classical approaches, PEPs in general
Additional optimizations

## Slide 2: Motivation for Mobile IP
Routing
  based on IP destination address, network prefix (e.g. 129.13.42) determines physical subnet
  change of physical subnet implies change of IP address to have a topological correct address (standard IP) or needs special entries in the routing tables
Specific routes to end-systems?
  change of all routing table entries to forward packets to the right destination
  does not scale with the number of mobile hosts and frequent changes in the location, security problems
Changing the IP-address?
  adjust the host IP address depending on the current location
  almost impossible to find a mobile system, DNS updates take to long time
  TCP connections break, security problems

## Slide 3: Requirements for Mobile IPv4 (RFC 5944 was: 3344, was: 3220, was: …, updated by: …)
Transparency
  mobile end-systems keep their IP address
  continuation of communication after interruption of link possible
  point of connection to the fixed network can be changed
Compatibility
  support of the same layer 2 protocols as IP
  no changes to current end-systems and routers required
  mobile end-systems can communicate with fixed systems
Security
  authentication of all registration messages
Efficiency and scalability
  only few additional messages to the mobile system required (connection typically via a low bandwidth radio link)
  world-wide support of a large number of mobile systems in the whole Internet

## Slide 4: Terminology
Mobile Node (MN)
  system (node) that can change the point of connection to the network without changing its IP address
Home Agent (HA)
  system in the home network of the MN, typically a router
  registers the location of the MN, tunnels IP datagrams to the COA
Foreign Agent (FA)
  system in the current foreign network of the MN, typically a router
  forwards the tunneled datagrams to the MN, typically also the default router for the MN
Care-of Address (COA)
  address of the current tunnel end-point for the MN (at FA or MN)
  actual location of the MN from an IP point of view
  can be chosen, e.g., via DHCP
Correspondent Node (CN)
  communication partner

## Slide 5: Example network
mobile end-system
Internet
router
router
router
end-system
FA
HA
MN
home network
foreign network
(physical home network
for the MN)
(current physical network for the MN)
CN

## Slide 6: Data transfer to the mobile system
Internet
sender
FA
HA
MN
home network
foreign
network
receiver
1
2
3
1. Sender sends to the IP address of MN,
HA intercepts packet (proxy ARP)
2. HA tunnels packet to COA, here FA,
by encapsulation
3. FA forwards the packet to the MN
CN

## Slide 7: Data transfer from the mobile system
Internet
receiver
FA
HA
MN
home network
foreign network
sender
1
1. Sender sends to the IP address of the receiver as usual, FA works as default router
CN

## Slide 8: Overview
CN
router
HA
router
FA
Internet
router
1.
2.
3.
home
network
MN
foreign
network
4.
CN
router
HA
router
FA
Internet
router
home
network
MN
foreign
network
COA

## Slide 9: Questions & Tasks
  What is the key motivation for the classical Mobile IP?
  Why can we use mobile systems without any Mobile IP?
  What is triangular routing? Potential performance issues?

## Slide 10: Network integration
Agent Advertisement
  HA and FA periodically send advertisement messages into their physical subnets
  MN listens to these messages and detects, if it is in the home or a foreign network (standard case for home network)
  MN reads a COA from the FA advertisement messages
Registration (always limited lifetime!)
  MN signals COA to the HA via the FA, HA acknowledges via FA to MN
  these actions have to be secured by authentication
Advertisement
  HA advertises the IP address of the MN (as for fixed systems), i.e. standard routing information
  routers adjust their entries, these are stable for a longer time (HA responsible for a MN over a longer period of time)
  packets to the MN are sent to the HA,
  independent of changes in COA/FA

## Slide 11: Agent advertisement
Extended ICMP Router Advertisements
type = 16
length = 6 + 4 * #COAs
R: registration required
B: busy, no more registrations
H: home agent
F: foreign agent
M: minimal encapsulation
G: GRE encapsulation
r: =0, ignored (former Van Jacobson compression)
T: FA supports reverse tunneling
reserved: =0, ignored
preference level 1
router address 1
#addresses
type
addr. size
lifetime
checksum
COA 1
COA 2
type = 16
sequence number
length
0
7
8
15
16
31
24
23
code
preference level 2
router address 2
. . .
registration lifetime
. . .
R
B
H
F
M
G
r
reserved
T

## Slide 12: Registration
t
MN
HA
registration
request
registration
reply
t
MN
FA
HA
registration
request
registration
request
registration
reply
registration
reply

## Slide 13: Mobile IP registration request
home agent
home address
type = 1
lifetime
0
7
8
15
16
31
24
23
T x
identification
COA
extensions . . .
S
B
D
M
G
r
S: simultaneous bindings
B: broadcast datagrams
D: decapsulation by MN
M mininal encapsulation
G: GRE encapsulation
r: =0, ignored
T: reverse tunneling requested
x: =0, ignored

## Slide 14: Mobile IP registration reply
home agent
home address
type = 3
lifetime
0
7
8
15
16
31
code
identification
extensions . . .
Example codes:
registration successful
0 registration accepted
1 registration accepted, but simultaneous mobility bindings unsupported
registration denied by FA
65 administratively prohibited
66 insufficient resources
67 mobile node failed authentication
68 home agent failed authentication
69 requested Lifetime too long
registration denied by HA
129 administratively prohibited
131 mobile node failed authentication
133 registration Identification mismatch
135 too many simultaneous mobility bindings

## Slide 15: Encapsulation – needed for the tunnel HA-CoA
original IP header
original data
new data
new IP header
outer header
inner header
original data

## Slide 16: Encapsulation
Encapsulation of one packet into another as payload
  e.g. IPv6 in IPv4 (6Bone), Multicast in Unicast (Mbone)
  here: e.g. IP-in-IP-encapsulation, minimal encapsulation or GRE (Generic Record Encapsulation)
IP-in-IP-encapsulation (mandatory, RFC 2003)
  tunnel between HA and COA
Care-of address COA
IP address of HA
TTL
IP identification
IP-in-IP
IP checksum
flags
fragment offset
length
DS (TOS)
ver.
IHL
IP address of MN
IP address of CN
TTL
IP identification
lay. 4 prot.
IP checksum
flags
fragment offset
length
DS (TOS)
ver.
IHL
TCP/UDP/ ... payload

## Slide 17: Optional: Generic Routing Encapsulation
original
header
original data
new data
new header
outer header
GRE header
original data
original header
Care-of address COA
IP address of HA
TTL
IP identification
GRE
IP checksum
flags
fragment offset
length
DS (TOS)
ver.
IHL
IP address of MN
IP address of CN
TTL
IP identification
lay. 4 prot.
IP checksum
flags
fragment offset
length
DS (TOS)
ver.
IHL
TCP/UDP/ ... payload
routing (optional)
sequence number (optional)
key (optional)
offset (optional)
checksum (optional)
protocol
rec.
rsv.
ver.
C
R
K
S
s
RFC 1701
RFC 2784 (updated by 2890)
reserved1 (=0)
checksum (optional)
protocol
reserved0
ver.
C

## Slide 18: Optimization of packet forwarding
Problem: Triangular Routing
  sender sends all packets via HA to MN
  higher latency and network load
“Solutions”
  sender learns the current location of MN
  direct tunneling to this location
  HA informs a sender about the location of MN
  big security problems!
Change of FA
  packets on-the-fly during the change can be lost
  new FA informs old FA to avoid packet loss, old FA now forwards remaining packets to new FA
  this information also enables the old FA to release resources for the MN

## Slide 19: Change of foreign agent
CN
HA
FAold
FAnew
MN
MN changes location
t
Data
Data
Data
Update
ACK
Data
Data
Registration
Update
ACK
Data
Data
Data
Warning
Request
Update
ACK
Data
Data

## Slide 20: Reverse tunneling (RFC 3024, was: 2344)
Internet
receiver
FA
HA
MN
home network
foreign network
sender
3
2
1
1. MN sends to FA
2. FA tunnels packets to HA
by encapsulation
3. HA forwards the packet to the
receiver (standard case)
CN

## Slide 21: Mobile IP with reverse tunneling
Router accept often only “topological correct“ addresses (firewall!)
  a packet from the MN encapsulated by the FA is now topological correct
  furthermore multicast and TTL problems solved (TTL in the home network correct, but MN is to far away from the receiver)
Reverse tunneling does not solve
  problems with firewalls, the reverse tunnel can be abused to circumvent security mechanisms (tunnel hijacking)
  optimization of data paths, i.e. packets will be forwarded through the tunnel via the HA to a sender (double triangular routing)
The standard is backwards compatible
  the extensions can be implemented easily and cooperate with current implementations without these extensions
  Agent Advertisements can carry requests for reverse tunneling

## Slide 22: Problems with mobile IP
Security
  authentication with FA problematic, for the FA typically belongs to another organization
  no common protocol for key management and key distribution widely accepted in the Internet
Firewalls
  typically mobile IP cannot be used together with firewalls, special set-ups are needed (such as reverse tunneling)
QoS
  many new reservations in case of resource reservation protocols
  tunneling makes it hard to give a flow of packets a special treatment needed for the QoS
Security, firewalls, QoS etc. are always topics of research and discussions…

## Slide 23: Questions & Tasks
  How does an MN detect that it is not “at home”?
  What is the difference of a co-located COA and a COA at the FA?
  How to optimize triangular routing?
  Why may reverse tunneling be needed? Performance issues?
  Which security issues come with mobile IP?

## Slide 24: Mobile IP and IPv6 (RFC 6275, was: 3775)
Mobile IP was developed for IPv4, but IPv6 simplifies the protocols
  security is integrated and not an add-on, authentication of registration is included
  COA can be assigned via auto-configuration (DHCPv6 is one candidate), every node has address auto-configuration
All routers perform router advertisement
  can be used instead of the special agent advertisement, no need for a separate FA
Addresses are always co-located
  MN can signal a sender directly the COA, sending via HA not needed in this case
  this allows for an automatic path optimization
„Soft“ hand-over
  no packet loss due to change of subnets
  MN sends the new COA to its old router
  the old router encapsulates all incoming packets for the MN and forwards them to the new COA
  authentication is always granted

## Slide 25: IP Micro-mobility support
What happens if, e.g., a student changes subnets on a campus frequently?
  Involvement of the HA each time
  Reveals precise “location”
Micro-mobility support:
  Efficient local handover inside a foreign domain without involving a home agent
  Reduces control traffic on backbone
  Especially needed in case of route optimization
Lot of research, not everything in products
Important criteria: Security Efficiency, Scalability, Transparency, Manageability

## Slide 26: Hierarchical Mobile IPv6 (RFC 5380, was: 4140)
Operation:
  Network contains mobility anchor point (MAP)
    mapping of regional COA (RCOA) to link COA (LCOA)
  Upon handover, MN informs MAP only
    gets new LCOA, keeps RCOA
  HA is only contacted if MAP changes
Security provisions:
  no HMIP-specific security provisions
  binding updates should be authenticated
MAP
Internet
AR
MN
AR
MN
HA
binding
update
RCOA
LCOAold
LCOAnew

## Slide 27: Hierarchical Mobile IP: Security
Advantages:
  Local COAs can be hidden, which provides at least some location privacy
  Direct routing between CNs sharing the same link is possible (but might be dangerous)
  Handover requires minimum number of overall changes to routing tables
Potential problems:
  Decentralized security-critical functionality (handover processing) in mobility anchor points
  MNs can (must!) directly influence routing entries via binding updates (authentication necessary)
  Not transparent to MNs
  Handover efficiency in wireless mobile scenarios:
    All routing reconfiguration messages sent over wireless link

## Slide 28: Proxy Mobile IPv6 (PMIPv6)
WLAN access
network
Network-based mobility management protocol, RFC5213, updated by RFC6543, RFC7864
  enables IP mobility for a host without requiring its participation in any mobility-related signaling
  the network manages the IP mobility, no software change in clients needed
  adopted by 3GPP in LTE (LMA is in the PDN Gateway, 3GPP TS 29.275)
Local Mobility Anchor (LMA)
  acts as MIPv6 Home Agent
  anchor for MN’s network prefix(es)
Mobile Access Gateway (MAG)
  function on access routers, tracks MN’s mobility
  performs the signaling in the network with the LMA
  does the mobility management on behalf of the MN
  compatible to MIPv6 enabled MNs
IP traffic offloading possible
CN
MN
MAG
Internet
3GPP
EPC
LMA
MAG
MAG
bi-directional tunnel

## Slide 29: Split the two roles of an IP address: localization and identification
Host Identity Protocol v2 (HIPv2, RFC 7401, was: 5201, updated by 6253, 8002)
  Introduction of HIP layer between routing and transport, Alternative to Mobile IP
  IP addresses for routing only, change depending on location (must be topological correct!)
  Identification via Host Identity Tag, used e.g. for TCP connection identification instead of IP address
  Host Identity Tag based on public keys
    Communication requires Diffie Hellman key exchange
  Pro
    No intermediate agent, normal IP routing
  Con
    Extra RTT due to key exchange, firewalls, extra layer
  See also RFCs 5202, 5203, 5204, 5205, 5206, 5207, 5770…
Locator/ID Separation Protocol (LISP, RFC 6830)
  New routing concept, tunneling for data transport, no changes to hosts or core
  RLOC (Routing Locator): topologically assigned, used for routing
  EID (Endpoint Identifier): administratively assigned, used for identification

## Slide 30: Questions & Tasks
  How does IPv6 simplify Mobile IP?
  What is the motivation of micro-mobility support?
  What is a big advantage of PMIPv6?
  Which two roles does an IP address have? Why can this be problematic? Solutions?

## Slide 31: Mobile ad hoc networks
Standard Mobile IP needs an infrastructure
  Home Agent/Foreign Agent in the fixed network
  DNS, routing etc. are not designed for mobility
Sometimes there is no infrastructure!
  remote areas, ad-hoc meetings, disaster areas
  cost can also be an argument against an infrastructure!
Main topic: routing
  no default router available
  every node should be able to forward
A
B
C

## Slide 32: Solution: Wireless ad-hoc networks
Network without infrastructure
  Use components of participants for networking
Examples
  Single-hop: All partners max. one hop apart
    Bluetooth piconet, tablets in a room, gaming devices…
  Multi-hop: Cover larger distances, circumvent obstacles
    Bluetooth scatternet, TETRA police network, car-to-car networks…
Internet: MANET (Mobile Ad-hoc Networking) group
  IEEE mesh networks solve similar issues on layer 2 – but think of layer 2 vs. layer 3 addresses!

## Slide 33: Manet: Mobile Ad-hoc Networking
Fixed
Network
Mobile
Devices
Mobile
Router
Manet
Mobile IP,
DHCP
Router
End system

## Slide 34: Problem No. 1: Routing
Highly dynamic network topology
  Device mobility plus varying channel quality
  Separation and merging of networks possible
  Asymmetric connections possible
good link
weak link
time = t1
time = t2
N1
N4
N2
N5
N3
N1
N4
N2
N5
N3
N6
N7
N6
N7

## Slide 35: Traditional routing algorithms
Distance Vector
  periodic exchange of messages with all physical neighbors that contain information about who can be reached at what distance
  selection of the shortest path if several paths available
Link State
  periodic notification of all routers about the current state of all physical links
  router get a complete picture of the network
Example
  ARPA packet radio network (1973), DV-Routing
  every 7.5s exchange of routing tables including link quality
  updating of tables also by reception of packets
  routing problems solved with limited flooding

## Slide 36: Routing in ad-hoc networks
Was THE big topic in many research projects
  Far more than 50, 100, 150, … different proposals exist
  The most simple one: Flooding!
Reasons
  Classical approaches from fixed networks fail
    Very slow convergence, large overhead
  High dynamicity, low bandwidth, low computing power
Metrics for routing
  Minimal
    Number of nodes, loss rate, delay, congestion, interference …
  Maximal
    Stability of the logical network, battery run-time, time of connectivity …

## Slide 37: Problems of traditional routing algorithms
Dynamic of the topology
  frequent changes of connections, connection quality, participants
Limited performance of mobile systems
  periodic updates of routing tables need energy without contributing to the transmission of user data, sleep modes difficult to realize
  limited bandwidth of the system is reduced even more due to the exchange of routing information
  links can be asymmetric, i.e., they can have a direction dependent transmission quality

## Slide 38: A simple example: Dynamic source routing I
Split routing into discovering a path and maintaining a path
Discover a path
  only if a path for sending packets to a certain destination is needed and no path is currently available
Maintaining a path
  only while the path is in use one has to make sure that it can be used continuously
No periodic updates needed! It is a so-called reactive routing protocol.

## Slide 39: A simple example: Dynamic source routing II
Path discovery
  broadcast a packet with destination address and unique ID
  if a station receives a broadcast packet
    if the station is the receiver (i.e., has the correct destination address) then return the packet to the sender (path was collected in the packet)
    if the packet has already been received earlier (identified via ID) then discard the packet
    otherwise, append own address and broadcast packet
  sender receives packet with the current path (address list)
Optimizations
  limit broadcasting if maximum diameter of the network is known
  caching of address lists (i.e. paths) with help of passing packets
    stations can use the cached information for path discovery (own paths or paths for other hosts)

## Slide 40: DSR: Route Discovery
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
Sending from C to O

## Slide 41: DSR: Route Discovery
Broadcast
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
[O,C,4711]
[O,C,4711]

## Slide 42: DSR: Route Discovery
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
[O,C/G,4711]
[O,C/G,4711]
[O,C/B,4711]
[O,C/E,4711]

## Slide 43: DSR: Route Discovery
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
[O,C/G/I,4711]
[O,C/B/A,4711]
[O,C/B/D,4711]
[O,C/E/H,4711]
(alternatively: [O,C/E/D,4711])

## Slide 44: DSR: Route Discovery
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
[O,C/B/D/F,4711]
[O,C/G/I/K,4711]
[O,C/E/H/J,4711]

## Slide 45: DSR: Route Discovery
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
[O,C/E/H/J/L,4711]
(alternatively: [O,C/G/I/K/L,4711])
[O,C/G/I/K/M,4711]

## Slide 46: DSR: Route Discovery
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
[O,C/E/H/J/L/N,4711]

## Slide 47: DSR: Route Discovery
B
A
C
G
I
D
K
L
E
H
F
J
Q
P
M
N
O
R
Path: M, K, I, G

## Slide 48: A simple example: Dynamic Source Routing III
Maintaining paths
  after sending a packet
    wait for a layer 2 acknowledgement (if applicable)
    listen into the medium to detect if other stations forward the packet (if possible)
    request an explicit acknowledgement
  if a station encounters problems it can inform the sender of a packet or look-up a new path locally

## Slide 49: Interference-based routing
Routing based on assumptions about interference between signals
S1
N5
N3
N4
N1
N2
R1
R2
N6
N8
S2
N9
N7
neighbors
(i.e. within radio range)

## Slide 50: A plethora of ad hoc routing protocols
Flat
  proactive
    FSLS – Fuzzy Sighted Link State
    FSR – Fisheye State Routing
    OLSR – Optimized Link State Routing Protocol (RFC 3626)
    TBRPF – Topology Broadcast Based on Reverse Path Forwarding
  reactive
    AODV – Ad hoc On demand Distance Vector (RFC 3561)
    DSR – Dynamic Source Routing (RFC 4728)
    DYMO – Dynamic MANET On-demand
Hierarchical
  CGSR – Clusterhead-Gateway Switch Routing
  HSR – Hierarchical State Routing
  LANMAR – Landmark Ad Hoc Routing
  ZRP – Zone Routing Protocol
Geographic position assisted
  DREAM – Distance Routing Effect Algorithm for Mobility
  GeoCast – Geographic Addressing and Routing
  GPSR – Greedy Perimeter Stateless Routing
  LAR – Location-Aided Routing
OLSRv2: RFC 7181
updated by 7183, 7187, 7188, 7466
table-driven, proactive
optimization of classic link state routing
selection of multipoint-relays (MPRs): each 2-hop neighbor must be reachable
flooding of topology messages only via MPRs
different link metrics possible

## Slide 51: Further difficulties and research areas
Auto-Configuration
  Assignment of addresses, function, profile, program, …
Service discovery
  Discovery of services and service providers
Multicast
  Transmission to a selected group of receivers
Quality-of-Service
  Maintenance of a certain transmission quality
Power control
  Minimizing interference, energy conservation mechanisms
Security
  Data integrity, protection from attacks (e.g. Denial of Service)
Scalability
  10 nodes? 100 nodes? 1000 nodes? 10000 nodes?
Integration with fixed networks
Internet
Super cluster
Cluster
Base station
Cluster head

## Slide 52: Questions & Tasks
  What makes routing so difficult in ad-hoc networks?
  Which problems do traditional routing algorithms have in wireless ad-hoc networks?
  What is the difference between proactive and reactive routing protocols?
  What are metrics for wireless ad-hoc routing?

## Slide 53: The next step: Wireless Sensor Networks (WSN)
Commonalities with MANETs
  Self-organization, multi-hop
  Typically wireless, should be energy efficient
Differences to MANETs
  Applications: MANET more powerful, more general  WSN more specific
  Devices: MANET more powerful, higher data rates, more resources  WSN rather limited, embedded, interacting with environment
  Scale: MANET rather small (some dozen devices)  WSN can be large (thousands)
  Basic paradigms: MANET individual node important, ID centric  WSN network important, individual node may be dispensable, data centric
  Mobility patterns, Quality-of Service, Energy, Cost per node …

## Slide 54: Properties of wireless sensor networks
Sensor nodes (SN) monitor and control the environment
Nodes process data and forward data via radio
Integration into the environment, typically attached to other networks over a gateway (GW)
Network is self-organizing and energy efficient
Potentially high number of nodes at very low cost per node
SN
GW
SN
SN
SN
SN
SN
SN
SN
SN
SN
SN
GW
GW
GW
Bluetooth, TETRA, …
Ethernet
SN
GPRS
WLAN
ALARM!
ALARM!
ALARM!
ALARM!
Notes: 54

## Slide 55: Promising applications for WSNs
Machine and vehicle monitoring
  Sensor nodes in moveable parts
  Monitoring of hub temperatures, fluid levels …
Health & medicine
  Long-term monitoring of patients with minimal restrictions
  Intensive care with relative great freedom of movement
Intelligent buildings, building monitoring
  Intrusion detection, mechanical stress detection
  Precision HVAC with individual climate
Environmental monitoring, person tracking
  Monitoring of wildlife and national parks
  Cheap and (almost) invisible person monitoring
  Monitoring waste dumps, demilitarized zones
… and many more: logistics (total asset management, RFID), telematics …
  WSNs are quite often complimentary to fixed networks!
Notes: 55

## Slide 56: And now… the Internet of Things!

## Slide 57: Internet of Things – is it really new?
1991: Mark Weiser
  The Computer for the 21st Century, ubiquitous use of IT, disappearing computer
1999: Kevin Ashton
  Coined the term Internet of Things in the context of logistics/supply chains, enhanced radio tags
Network of inter-connected, embedded mini computers
  Collecting and distributing data, Internet technologies as common platform, comprises enhanced RFIDs, wireless sensor networks, actors, mobile communications, “smart” objects, cyber physical systems, …
  Next generation embedded systems + wireless sensor networks + actors + Internet protocols + …
Already today, there are many more communicating systems compared to people – more than 10 billion
In the future:
  Some estimate > 25 billion end of 2020, others estimate > 50 billion – ok, there will be MANY…
  As always great expectations: 202x - 1 trillion $ revenue p.a. estimated by GSMA

## Slide 58: Internet of Things: What is really new?
Miniaturization
  MEMS, smart everything, embedded objects
Availability of many “new” technologies
  Cloud/edge computing, big data, IPv6, 6LoWPAN, content centric networking, adapted operating systems…
Restricted devices
  At least at the beginning wrt. firewalls, antivirus, …
  BUT we all use the same or similar protocols and interfaces
Complexity
  function(#nodes, topology, traffic pattern, stability, legacy, ?)
 All this comes together now! Possibilities and vulnerabilities…
Source: RIOT OS, www.riot-os.org
1,5 kByte RAM, 5 kByte ROM,
real-time, multi-threaded
© iecetech.org

## Slide 59: 6LoWPAN
IPv6 over Low power Wireless Personal Area Networks
  RFCs (updates): 4919, 4944 (6282, 6775, 8025, 8066), 6282 (8066), 6775 (8505), 6606, 6568
Assumptions: IEEE 802.15.4 devices are limited in power/memory/energy, have long sleep cycles, are unreliable, ad-hoc deployment is typical, large number of devices will be seen, …
Problem:
  MAC layer offers only max. 81 byte for data due to PHY limits plus security mechanisms
  IPv6 header requires 40 byte, UDP additional 8 byte, leaving only 33 byte for applications
Solution:
  Compression of IPv6 and UDP headers down to 7 byte (ideal case)
  Fragmentation of packets as IPv6 requires at least 1280 byte message size
  Adaptation layer between link and network layer
802.15.4
AES
IPv6
UDP
payload
FCS
802.15.4
AES
IPv6
UDP
payload
FCS
D
byte
byte
23
21
40
8
33
2
23
21
2-7
4
70-75
2
D: dispatch, defines packet type (e.g., IPv6 adr., fragment, mesh…)

## Slide 60: Questions & Tasks
  Think of mobile and wireless communications – what are specific challenges of WSNs or IoT in general?
  Which problems arise using the classical Internet protocols together with e.g. 802.15.4/ZigBee?

## Slide 61: The Transport Layer
Example: HTTP (used by web services) typically uses TCP
  Reliable transport between client and server required
TCP
  Steam oriented, not transaction oriented
  Network friendly: time-out  congestion  slow down transmission
Well known – TCP guesses quite often wrong in wireless and mobile networks
  Packet loss due to transmission errors
  Packet loss due to change of network
Result
  Severe performance degradation
Client
Server
Connection
setup
Data
transmission
Connection
release
TCP SYN
TCP SYN/ACK
TCP ACK
HTTP request
HTTP response
GPRS: 500ms!
>15 s
no data

## Slide 62: Motivation I
Transport protocols typically designed for
  Fixed end-systems
  Fixed, wired networks
Research activities
  Performance
  Congestion control
  Efficient retransmissions
TCP congestion control
  packet loss in fixed networks typically due to (temporary) overload situations
  router have to discard packets as soon as the buffers are full
  TCP recognizes congestion only indirect via missing acknowledgements, retransmissions unwise, they would only contribute to the congestion and make it even worse
  slow-start algorithm as reaction

## Slide 63: Motivation II
TCP slow-start algorithm
  sender calculates a congestion window for a receiver
  start with a congestion window size equal to one segment
  exponential increase of the congestion window up to the congestion threshold, then linear increase
  missing acknowledgement causes the reduction of the congestion threshold to one half of the current congestion window
  congestion window starts again with one segment
TCP fast retransmit/fast recovery
  TCP sends an acknowledgement only after receiving a packet
  if a sender receives several acknowledgements for the same packet, this is due to a gap in received packets at the receiver
  however, the receiver got all packets up to the gap and is actually receiving packets
  therefore, packet loss is not due to congestion, continue with current congestion window (do not use slow-start)

## Slide 64: Influences of mobility on TCP-mechanisms
TCP assumes congestion if packets are dropped
  typically wrong in wireless networks, here we often have packet loss due to transmission errors
  furthermore, mobility itself can cause packet loss, if e.g. a mobile node roams from one access point (e.g. foreign agent in Mobile IP) to another while there are still packets in transit to the wrong access point and forwarding is not possible
The performance of an unchanged TCP can degrade severely
  however, TCP cannot be changed fundamentally due to the large base of installations in the fixed network, TCP for mobility has to remain compatible
  the basic TCP mechanisms keep the whole Internet together

## Slide 65: Early approach: Snooping TCP I
“Transparent” extension of TCP within the foreign agent
  buffering of packets sent to the mobile host
  lost packets on the wireless link (both directions!) will be retransmitted immediately by the mobile host or foreign agent, respectively (so called “local” retransmission)
  the foreign agent therefore “snoops” the packet flow and recognizes acknowledgements in both directions, it also filters ACKs
  changes of TCP only within the foreign agent
„wired“ Internet
buffering of data
end-to-end TCP connection
local retransmission
correspondent
host
foreign
agent
mobile
host
snooping of ACKs

## Slide 66: Early approach: Snooping TCP II
Data transfer to the mobile host
  FA buffers data until it receives ACK of the MH, FA detects packet loss via duplicated ACKs or time-out
  fast retransmission possible, transparent for the fixed network
Data transfer from the mobile host
  FA detects packet loss on the wireless link via sequence numbers, FA answers directly with a NACK to the MH
  MH can now retransmit data with only a very short delay
Integration of the MAC layer
  MAC layer often has similar mechanisms to those of TCP
  thus, the MAC layer can already detect duplicated packets due to retransmissions and discard them
Problems
  snooping TCP does not isolate the wireless link as good as other approaches (e.g. Indirect-TCP)
  snooping might be useless depending on encryption schemes

## Slide 67: Fast retransmit/fast recovery
Change of foreign agent often results in packet loss
  TCP reacts with slow-start although there is no congestion
Forced fast retransmit
  as soon as the mobile host has registered with a new foreign agent, the MH sends duplicated acknowledgements on purpose
  this forces the fast retransmit mode at the communication partners
  additionally, the TCP on the MH is forced to continue sending with the actual window size and not to go into slow-start after registration
Advantage
  simple changes result in significant higher performance
Disadvantage
  further mix of IP and TCP, no transparent approach

## Slide 68: Transmission/time-out freezing
Mobile hosts can be disconnected for a longer time
  no packet exchange possible, e.g., in a tunnel, disconnection due to overloaded cells or multiplexing with higher priority traffic
  TCP disconnects after time-out completely
TCP freezing
  MAC layer is often able to detect interruption in advance
  MAC can inform TCP layer of upcoming loss of connection
  TCP stops sending, but does now not assume a congested link
  MAC layer signals again if reconnected
Advantage
  scheme is independent of data
Disadvantage
  TCP on mobile host has to be changed, mechanism depends on MAC layer

## Slide 69: Selective retransmission
TCP acknowledgements are often cumulative
  ACK n acknowledges correct and in-sequence receipt of bytes up to n-1 (byte-stream oriented!)
  if single packets are missing quite often a whole packet sequence beginning at the gap has to be retransmitted (go-back-n), thus wasting bandwidth
Selective retransmission as one solution
  RFC2018 allows for acknowledgements of single packets, not only acknowledgements of in-sequence packet streams without gaps
  sender can now retransmit only the missing packets (i.e. non acknowledged parts of the byte-stream)
Advantage
  much higher efficiency
“Disadvantage”
  more complex software in a receiver, more buffer needed at the receiver
  Might be a problem in really tiny devices…

## Slide 70: Comparison of different approaches for a “mobile” TCP

## Slide 71: TCP Improvements I
Initial research work
  Indirect TCP, Snoop TCP, M-TCP, T/TCP, SACK, Transmission/time-out freezing, …
TCP over 2.5/3G wireless networks
  Fine tuning of TCP, RFC3481 – best current practice (BCP 71, 2003)
  Learn to live with sometimes
    Data rates: 64 kbit/s up, 115-384 kbit/s down; asymmetry: 3-6, but also up to 1000 (broadcast systems), periodic allocation/release of channels
    High latency, high jitter, packet loss
  Suggestions
    Large (initial) sending windows, large maximum transfer unit, selective acknowledgement, explicit congestion notification, time stamp, no header compression
  Widespread use in adapted protocol stacks
    “Historical”: i-mode running over FOMA, WAP 2.0 (“TCP with wireless profile”)
  Alternative congestion control algorithms
    TCP Vegas (cong. control with focus on packet delay, rather than packet loss)
    TCP Westwood plus (use ACK stream for better setting cong. control), (New) Reno, Santa Cruz, …
max. TCP BandWidth
Max. Segment Size
Round Trip Time
loss probability

## Slide 72: TCP Improvements II
Performance enhancing proxies (PEP, RFC 3135)
  Transport layer
    Local retransmissions and acknowledgements
  Additionally on the application layer
    Content filtering, compression, picture downscaling
    E.g., Internet/WAP gateways
    Web service gateways?
  Big problem: breaks end-to-end semantics
    Disables use of IP security
    Choose between PEP and security!
More open issues
  RFC 3150 / BCP 48 (slow links)
    Recommends header compression, no timestamp
  RFC 3155 / BCP 50 (links with errors)
    States that explicit congestion notification cannot be used
  In contrast to 2.5G/3G recommendations!
Mobile system
PEP
Comm. partner
wireless
Internet

## Slide 73: Questions & Tasks
  What are the problems of using TCP over wireless links?
  Why do many “enhancements” fail or are not wide-spread?
  What should wireless systems optimize in favor of TCP performance?