## Slide 1: Mobile Communications Chapter 7 : Outlook
The future of mobile and wireless networks – Is it 5G/6G/…?
All IP? Licensed? Public? Private? Micro-operators? Trillions of devices?
Tbit/s connections with sub ms latency? AI everywhere? Wireless tactile Internet?

## Slide 2: Mobile and wireless services – Remember: Always Best Connected
UMTS
2 Mbit/s
LTE
10 Mbit/s
LAN
100 Mbit/s,
WLAN
54 Mbit/s
LTE, UMTS
2 Mbit/s
GSM 115 kbit/s,
WLAN 11 Mbit/s
GSM 53 kbit/s
Bluetooth 500 kbit/s
GSM/EDGE 384 kbit/s,
WLAN 5 Mbit/s
LAN, WLAN
100 Mbit/s

## Slide 3: Wireless systems: overview of the (historical) development
cellular phones
satellites
wireless LAN
cordless phones
1992:
GSM
1994: DCS 1800
2001:
IMT-2000
1987: CT1+
1982:
Inmarsat-A
1992:
Inmarsat-B
Inmarsat-M
1998:
Iridium
1989:
CT 2
1991:
DECT
199x:
proprietary
1997:
IEEE 802.11
1999:
802.11b, Bluetooth
1988:
Inmarsat-C
analogue
digital
1991:
D-AMPS
1991:
CDMA
1981:
NMT 450
1986:
NMT 900
1980: CT0
1984: CT1
1983:
AMPS
1993:
PDC
2000: GPRS
2000:
IEEE 802.11a
2014:
Fourth Generation
(Internet based)

## Slide 4: New: Convergence with new applications
Internet of things
Industrial control systems
Power grid
Medical devices
Autonomous vehicles
…
Fixed networks
„Classical“
Internet
Cable networks
Mobile networks
Company networks
Home networks
Common technology
(everything over IP)
UMS
PSTN
ISDN
DSL
GSM
GPRS
UMTS
LTE
FTP
P2P
WWW
Web2
Broadcast
VoD
iTV
Content
Sharing
WiFi
proprietary
VoIP
IPTV
3/4/5G
Communities

## Slide 5: Overlay Networks - the global goal
regional
metropolitan area
campus-based
in-car,
in-house,
personal area
vertical
handover
horizontal
handover
integration of heterogeneous fixed and mobile networks with varying transmission characteristics

## Slide 6: Wireless access technologies
DAB
802.11a/g/n/ac/ax
relative speed [km/h]
250
100
50
5
0
10 kbit/s
2 Mbit/s
20 Mbit/s
>1 Gbit/s
DECT
UMTS
GSM, TETRA
bandwidth
802.11b
Bluetooth
Point-to-multipoint distribution systems
physical/
economic border
EDGE
500
LTE
5G
New radios

## Slide 7: New applications
Source: GSMA Intelligence

## Slide 8: Software Defined Mobile Networking
  Apply SDN to mobile networks
    Dynamic, efficient network configuration
    Improved performance
    Separation of data (forwarding) and control (“brain”) plane
  Can be complemented by NFV
    Network Function Virtualization
    Virtualized network functions (SW implementations of network functions)
    Services can be built by chaining VNFs
    SDN could orchestrate and manage NFV
Source: Rost et. Al, Mobile Network Architecture Evolution toward 5G, IEEE Communications Magazine, vol. 54, no. 5, 2016

## Slide 9: ITU IMT-2020 – Applications for 5G
Source: ITU, M.2083
URLL
mMTC
eMBB

## Slide 10: ITU IMT-2020 – Performance Requirements
Source: ITU, M.2083

## Slide 11: ITU IMT-2020 – 3 main usage scenarios: eMBB, eMTC, URLL
Source: ITU, M.2083

## Slide 12: 3GPP LTE standardization roadmap toward 5G
Source: Rost et. Al, Mobile Network Architecture Evolution toward 5G, IEEE Communications Magazine, vol. 54, no. 5, 2016

## Slide 13: Some new 5G features
Using higher frequencies
  mmWave, operating bands up to 52.6 GHz, channel bandwidth up to 400 MHz, 30 bit/s/Hz down, 15 bit/s/Hz up
Variety of use cases
  scaling data rates from kbit/s up to Gbit/s
Mini-slots
  low latency response for, e.g., autonomous cars, factory automation
eMBB: 500 km/h mobility, 10-20 Gbit/s peak, all data all the time available
URLL: < 1ms air interface latency, 5 ms end-to-end latency (well, not around the globe, rather edge computing), 99.9999% reliability, 50 kbit/s-10 Mbit/s
mMTC: billions of things connected, ultra low cost, low energy, 105 to 106 devices per km², 1-100 kbit/s per device, 10 years battery life
Next Generation Core: uses SDN, NFV, SON – virtualization of network architecture

## Slide 14: New RAN architecture for 5G (3GPP TR 38.912)
gNodeB (gNB, next generation Node B)
  providing the New RAN U-plane and C-plane protocol terminations towards the UE
LTE eNode B (eNB)
  providing the E-UTRA U-plane and C-plane protocol terminations towards the UE.
Xn interface
  interconnection of nodes in New RAN with each other
NG interface
  connections of nodes in New RAN to the NGC
  supporting a many-to-many relation between NG-CP (Control Plane)/UPGWs (User Plane Gateways) and the nodes in New RAN
Source: ETSI TR 138 912

## Slide 15: LTE – New Radio co-existence (ETSI TR 138 912)
Source: ETSI TR 138 912

## Slide 16: 5G gets real in many places 2017/2018
At least some test installations, first devices – smooth transition
More realistic expectations in industry: „no fundamental difference between 4G and 5G“, „natural evolution“ – investment in 5G, but not big hype
Products that integrate 2G, 3G, 4G and 5G are available; smartphones available since 2019
Examples:
Berlin, 70 basestations operating at 3.7 GHz (5G New Radio), 64 antenna massive MIMO, beamforming, > 2 Gbit/s per client, RTT 7-9 ms
https://5g-ppp.eu/ for many more 5G trials
Source: Samsung

## Slide 17: 5G Evolution continues
Source: www.nttdocomo.co.jp, 6G Whitepaper

## Slide 18: Why needing more than 5G?
Source: www.nttdocomo.co.jp, 6G Whitepaper

## Slide 19: Extreme requirements for specific scenarios
Source: www.nttdocomo.co.jp, 6G Whitepaper

## Slide 20: 6G – The next step for 2030 and beyond - IMT-2030
Source: www.nttdocomo.co.jp, 6G Whitepaper

## Slide 21: Roadmap through the generations
Source: www.nttdocomo.co.jp, 6G Whitepaper

## Slide 22: LoRaWAN – a wireless technology for IoT I
LoRaWAN
Max. 250 mW, max. 1% duty cycle, ISM/SRD band (e.g. 433, 868 MHz)
Open specification, based on proprietary chirp spread spectrum technology (LoRa, Semtech Corp.)
Asymmetric, > 10km range, up to 50 kbit/s, star topology
LoRaAlliance
500+ member companies, solutions, products, services based on LoRaWAN
https://www.lora-alliance.org/
Open issues
LoRa closed, no open documentation
Doubts regarding scalability: “Do LoRa Low-Power Wide-Area Networks Scale?” (Bor et. Al, MSWiM’16)
  Typical smart city deployment supports only 3-4 nodes per 1000m² (20 byte packet every 16 min)
No hard guarantees for QoS

## Slide 23: LoRaWAN – a wireless technology for IoT II
LoRaWAN
https://www.thethingsnetwork.org/
https://www.ttnmapper.org/

## Slide 24: Many more wireless networks for IoT are evolving – who will make it?
www.electronicspecifier.com

## Slide 25: …and what about security? Availability?
„The Internet of Things (IoT) will present new attack surfaces as most of the IoT devices do not offer integrated security and, furthermore, it is often not possible to update security mechanisms later on. If compromised, these devices may serve as a backdoor for hackers to enter clinical IT systems – undiscovered for months.“ (DarkReading, www.informationweek.com, 22.12.16)
  Large variety of systems (hardware, interfaces, operating systems), typically “weak”
  Real interaction with the environment (CPS)
  Longer (but also much shorter!) life cycles, deeply embedded
  Complete unclear patching/updating strategy, responsibility
  How to integrate today the security needed in 30 years?
Software bugs do happen
  Even using the best software engineering principles
  Quite often due to unforeseeable interdependencies, new features, short innovation cycles
Often only one/very few vendors
  Even simple bugs may affect many networked systems
Result: very simple to affect millions of users
  System update @ German Telekom banned 40 million users from the network
  Simple misconfiguration at Internet routers cut off many autonomous systems
Classical high availability? Emergency calls? Redundancy?
Source: www.heise.de

## Slide 26: Questions & Tasks
  Is 5G all about higher data rates? What else do applications in the future need?
  What are the three main application domains of 5G?
  Why is even more than 5G needed? What could be applications?
  Check for LoRaWAN at your place. What else could be used for IoT? Pros and cons?
  This is not a security lecture – but think of vulnerabilities of mobile and wireless systems, think of the many systems depending on these networks…

## Slide 27: Thanks, take care – and have fun with Mobile Communications!
Source: Ed Jones/AFP, Seoul, South Korea,, 22.06.2016